3body problem, restricted & planar & circular

---
P
Rotating reference frame ω=n
r_2
r_1
y
x
B
ddot bold r + 2 (bold %omega times bold v) + bold %omega times (bold %omega times bold r) = - nabla V
bold %omega = left ( stack{0 # 0 # n} right )
bold v = left ( stack{dot x # dot y # dot z} right )
-Mass of test body=0
-Second body on circular orbit
-Planar (no inclination)
alignl color blue {ddot x - 2 n dot y = { partial U} over {partial x } }newline alignl color blue {ddot y + 2 n dot x = { partial U} over {partial y } } newline alignl color blue {ddot z = { partial U} over {partial z } } newline newline alignl color magenta {U = 1 over 2 n^2 ( x^2 + y^2) + %mu_1 over r_1 + %mu_2 over r_2 ``````````` Pseudo-potential}
Hill’s equations.
color teal {1 over 2 ( dot x^2 + dot y^2) = U + C over 2 `````````````` Jacoby `` constant}

---
alignl color blue {dot x ddot x - dot x 2 n dot y = dot x { partial U} over {partial x } }newline alignl color blue {dot y ddot y + dot y 2 n dot x = dot y { partial U} over {partial y } }
dot x ddot x + dot y ddot y = dot x { partial U} over {partial x } + dot y { partial U} over {partial y }
int from{t_0} to{t_1} (dot x ddot x + dot y ddot y) dt = int from{t_0} to{t_1} dot x { partial U} over {partial x } dt + int from{t_0} to{t_1} dot y { partial U} over {partial y } dt newline ```` drarrow ```` 1 over 2 ( dot x^2 + dot y^2) divides^{ x_1, y_1 }_{ x_0, y_0 } {} = int from{x_0} to{x_1} {{ partial U} over {partial x }} dx + int from{y_0} to{y_1} {{ partial U} over {partial y }} dy
1 over 2 dot x^2 + dot y^2 = U + C over 2
Normalized units:
alignl color red { G=1 ```````` G( m_1 + m_2 ) = 1} ````````` overline %mu = {alignc m_2} over { m_1 + m_2 } G newline alignl %mu_1 = G m_1 = 1 - overline %mu = x_2newline alignl %mu_2 = G m_2 = overline %mu = x_1 ``````````````` x_1 = overline %mu = {alignc m_2} over {m_1 + m_2 } ``````````x_2 = 1-x_1 newline alignl color red {a=1 }```````` n= sqrt{G (m_1+m_2) over {alignc a^3}} = 1
Adimensional numbers.

---
Hamiltonian approach
The Lagrangian of the system in the rotating reference frame is (kinetic energy minus potential energy):
L = T + V = 1 over 2 ( dot x^2 + dot y ^2 ) + U( x,y) + U_c (x,y )
L = 1 over 2 ( dot x^2 + dot y ^2 ) + left ( {1 - %mu} over r_1 right ) + %mu over r_2 + 1 over 2 ( x^2 + y^2 ) + x dot y - y dot x
The equations of motions are:
color green { d over dt { partial L } over { partial dot q_i } - { partial L } over {partial q_i} = 0 }
The Hamiltonian is:
H = sum from{i} p_i dot q_i - L(q_i, dot q_i,t) ````````````````where ````````````````p_i = { partial L } over { partial dot q_i }
color blue { p_x = { partial L } over { partial dot x} = dot x - y } newline alignl color blue { p_y = { partial L } over { partial dot y} = dot y + x}
alignl H = p_x dot x + p_y dot y - L = ` newline dot x^2 - dot x y + x dot y + dot y^2 - 1 over 2 ( dot x^2 + dot y^2 ) - U( x,y) - 1 over 2 (x^2 + y^2 ) - x dot y + y dot x = ` newline alignl color blue {1 over 2 (dot x^2 + dot y^2) - U(x,y) - 1 over 2 (x^2 + y^2) } = color red {1 over 2 v^2 - bar U(x,y)}
The Hamiltonian is the Jacoby integral

---
To go back to Hill’s equations from the Hamiltonian, Hamilton equations must be used:
alignl dot p_x = - {{partial H} over {partial x} } newline alignl dot x = {{partial H} over {partial p_x} }
alignl dot p_x = {partial L} over {partial x} = dot y + { partial overline {U} } over { partial x } newline alignl dot p_y = {partial L} over {partial y} = -dot x + { partial overline {U} } over { partial y } newline
alignl ddot x - 2 dot y = {{ partial overline {U} } over { partial x } } newline alignl ddot y + 2 dot x = {{ partial overline {U} } over { partial y } }
alignl ddot x - dot y = dot y + { partial overline {U} } over { partial x } newline alignl ddot y + dot x = dot x + { partial overline {U} } over { partial y } newline

---
Hill’s equations in normalized units
r2
r1
r1
y
x
S
P
μ
B
1-μ
x_1 = m over M x_2 = m over M ( 1 - x_1 ) ````` drarrow ````` x_1 ( M + m) = m ````` drarrow x_1 = m over { M+m} = overline %mu
alignl color blue {ddot x - 2 dot y = x - {(1 - overline {%mu})(x + overline %mu ) } over {alignc r_1^3 } - {overline %mu (1 - overline %mu - x) (-1 ) } over {alignc r_2^3 } }newline alignl color blue {ddot y + 2 dot x = y - {(1 - overline {%mu})y } over {alignc r_1^3 } - {overline %mu y } over {alignc r_2^3 } }
r_1 = sqrt {(x + overline %mu )^2 + y^2 } newline r_2 = sqrt {(x -1 + overline %mu )^2 + y^2 }
alignl color magenta {U(x,y) = 1 over 2 (x^2 + y^2) + (1- overline {%mu}) over {alignc r_1 } + {overline %mu } over {alignc r_2 } } newline W( x,y) = -U(x,y )

---
Lagrangian equilibrium points.
alignl color blue {ddot x =0 `````````` dot x = 0 }newline alignl color blue {ddot y = 0 `````````` dot y = 0 }
alignl color blue {nabla U = -nabla W = 0 }
alignl color blue {nabla U = bold r - {(1 - overline {%mu})bold r_1 } over {alignc r_1^3 } - {overline %mu bold r_2 } over {alignc r_2^3 } } newline alignl color blue {bold r = ( 1 - overline %mu ) bold r_1 + overline %mu bold r_2}
alignl color green {bold r = left( binom{x}{y} right ) ````` bold r_1 = left( binom{x + overline %mu}{alignc y} right ) ```` bold r_2 = left( binom{x -1 + overline %mu}{ alignc y} right) }
alignl color blue {(1 - overline %mu) bold r_1 left( 1 - 1 over r_1^3 right) + overline %mu bold r_2 left( 1 - 1 over r_2^3 right) = 0 }
Triangular Lagrangian points L4 and L5: r1 = r2 =1
Solving equation along x-axis L1, L2, L3:
alignl x = -1 -overline %mu + 7 over 12 overline %mu + O( {overline %mu}^3 ) `````````` color magenta { L_3 } newline alignl x = 1 -overline %mu +- left ( {overline %mu over 3 } right )^{1 over 3}+ O( {overline %mu}^{2 over 3} ) `````````` color magenta { L_1, ``L_2 }

---
alignl color blue {L_4 drarrow left( binom{1 over 2 - overline %mu}{sqrt 3 over {alignc 2} } right ) cdot a } newline alignl color blue {L_5 drarrow left( binom{1 over 2 - overline %mu}{- {sqrt 3 over {alignc 2}} } right ) cdot a }
Around these points move Trojan asteroids.
These lagrangian points define Hill’s sphere
alignl color blue {L_1 drarrow left( binom{1 - overline %mu + left( {overline %mu over 3} right)^{1 over 3}}{alignc 0} right ) cdot a } ``````````` color blue {L_2 drarrow left( binom{1 - overline %mu - left( {overline %mu over 3} right)^{1 over 3}}{alignc 0} right ) cdot a }
alignl color blue {L_3 drarrow left( binom{- 1 - 5 over 12 overline %mu} {alignc 0} right ) cdot a }

---
0 velocity curves: They cannot be crossed by a body!! They define the regions were stable motion is possible

---
Different curves for different value of the Jacoby constant C = 2U

---
Mars, Jupiter, Uranus and Neptune have Trojan asteroids.

---
Hill’s lobe: where the gravity of the body dominates respect to the central (more massive) body.
r_{ Hill } = 1 - %mu_2 + left( %mu_2 over 3 right )^{ 1/3 }
r_{ Hill } = left( {m_2 over {m_1 + m_2}} cdot {1 over 3} right )^{ 1/3 } cdot a
r_{ Hill }^{ Jupiter } = 0.355 ``au newline alignl r_{ Hill }^{ Earth } = 0.01 `` au
r_{ Roche} = R_M left( 2 %rho_M over %rho_m right )^( 1/3 ) ``````````R_M ``primary``body``````````

---
Cataclismic variables.

---
Tisserand invariant: an alias for the Jacoby constant in the sun reference frame….
The body velocity in the sun-centered reference frame is given by where v is the velocity in the rotating reference frame and vSR is velocity of the reference frame (the CM very closely matches the sun CM).
bold V = bold v + bold v_{SR}
With X and Y coordinates of the body in the sun-centered reference frame.
bold v_{SR} = left ( stack{ -n Y # n X} right )
The relation between the velocity components in the two reference frame is:
stack{ alignl{dot x } = dot X + n Y # alignl{dot y } = dot Y - n X # alignl{dot z} = dot Z }
We can add up the equations so that
(dot x^2 + dot y^2 + dot z^2) = (dot X^2 + dot Y^2 + dot Z^2) - 2 n (X dot Y - dot X Y) + n^2 (X^2 + Y^2)
1 over 2 v^2 = 1 over 2 V^2 - n h_z + {n^2} over 2 (X^2 + Y^2) = 1 over 2 V^2 - n h_z + {n^2} over 2 (x^2 + y^2)
Where hz is the angular momentum. Taking into account that X2 + Y2 = x2 + y2 and recalling the expression for the Jacoby constant we get:
1 over 2 v^2 - {n^2} over 2 (x^2 + y^2) = C + Gm_1 over r_1 + Gm_2 over r_2
1 over 2 V^2 -n h_z = C + Gm_1 over r_1 + Gm_2 over r_2

---
1 over 2 V^2 = Gm_1 left ( 1 over r_1 - 1 over 2a right )
Since
and
h_z = sqrt{ Gm_1 a (1 - e^2)} cos i
C + Gm_2 over r_2 = - G m_1 left( 1 over 2a + n sqrt{G m_1 a (1-e^2)} cos i right ) = - G m_1 left( 1 over 2a + sqrt{ {a (1-e^2)} over a_p^3} cos i right )
n is the mean motion of the planet. We can neglect the terms with m2 since m1>>m2 so:
color red { a_p over a +2 sqrt{ {a (1-e^2)} over a_p} cos i = T }
T is called the Tisserand parameter and it is approximately constant after an hyperbolic encounter with a planet.

---
From Hsieh & Haghighipour, 2016, Icarus, Volume 277, p. 19-38
Most comets have TJ < 3 while most asteroids have TJ > 3 but there are exceptions. Upper plot, comets in red with TJ < 3, on the bottom plot asteroids with TJ > 3 (blue dots)

---
P67: the comet explored by ROSETTA mission
The comet is made of two pieces (lobes) which independently formed in the outer Kuiper Belt.

---
Formed in the Kuiper Belt, due to repeated close encounters with Neptune it was injected in a elliptic orbit crossing the inner regions of the SS.

---
Close images of the comet surface.

---
A peculiar Plutino triple system: Lempo. Hiisi and Praha.

---
Trojan motion: effects of mass growth and migration of the planet. Trojan capture.
With nP mean motion of the planet, μ is the ratio mp/(mp + Ms), and φ the difference between between the longitude of the body and +/- π/3. This equation can be re-written in Hamiltonian form:
ddot %phi + 27 over 4 %mu n_P^2 %phi = 0
Where the libration frequency is given by
color red {H = 1 over 2 a_P^2 dot %phi^2 + 1 over 2 %omega^2 a_P^2 %phi^2 }
color red { %omega^2 = 27 over 4 %mu n_P^2} ````````````````````` %mu = m_P over { M_s + m_P }
It is the hamiltonian of a harmonic oscillator, the solution is
%phi( t) = A over 2 cos ( %omega t + %alpha )
Where A is the libration amplitude (the ½ is by definition of amplitude)
To test what it happens when we change either the semi-major axis or the mass of the planet we introduce an adiabatic invariant. The fast motion is the librational motion while the slow one is the change either in mass or semi-major axis of the planets.
The integration is performed in a circuit of the fast variable, assuming that in a period the relevant properties of the planet do not change i.e. aP, A and ω are costant over a period T. Since:
J = int to{period} p dq
p = a_P dot %phi ```````````````` q= a_P %phi

---
the integral becomes
J = int from{0} to{2 %pi} a_P dot %phi a_P d %phi = int from{0} to{T} a_P^2 A^2 over 4 %omega^2 sin^2( %omega t + %alpha) dt newline alignl J= a_P^2 A^2 over 4 %omega^2 int from{0} to{{2 %pi} over %omega} sin^2( %omega t + %alpha) dt
Recalling that
int sin^2(ax) dx = x over 2 - 1 over { 4a } sin ( 2 a x )
we get
alignl J= a_P^2 A^2 over 4 %omega^2 {2 %pi} over {2 %omega} = %pi over 4 A^2 a_P^2 %omega = ` ` newline %pi over 4 A^2 a_P^2 sqrt( 27 over 4 {m_P} over {m_P + M_s} ) sqrt( {G (m_P + M_s)} over a_P^3 ) = ` ` newline alignl %pi over 4 A^2 sqrt(27 over 4 G ) m_P^{ 1/2 } a_P^{ 1/2 }
The conservation of J in presence of adiabatic variations of both aP and mP leads to:
A_f over A_i = left ( a_{P,i} over a_{P,f} right )^(1/4) left ( m_{P,i} over m_{P,f} right )^(1/4)
This equation implies that either if the planet migrates inward or it grows in mass, the libration amplitude decreses (from Fleming & Hamilton, Icarus 148, 479, 2000) .