Evolution of circumstellar disks

---
ALMA: radiointerferometer → 66 radiotelescopes observing at millimiter and submillimter wavelength
Circumstellar disk in V1247 Orionis

---
HL Tau, age ~ 100000 yr, type: K9. Disk radius is about 2000 au and the mass is approximately 0.1 solar masses ( ALMA images, 0.3- 9.6 mm).

---
Disk around Elias 2-27 (age: 1 Myr, mass half of that of the sun) in the constellation of Ophiuchus at a distance of about 450 light years from Earth. The disk has spiral arms extending beyond 60 au from the star. Gravitational instability, binary companion or planet(s)?

---
Numerical modeling of the circumbinary disk in GG Tau (Nelson & Marzari, 2016)
Numerical modeling of a circumstellar disk in a binary star system (Picogna & Marzari, 2013)

---
Equation of fluid dynamics: Euler equations
1) Continuity equation: mass conservation
d over { dt } int from{V} %rho( bold r,t ) dV = - int from{S} ( %rho bold u ) cdot bold n ds newline alignl int from{V} {{partial %rho} over {partial t}} dV = - int from{V} nabla ( %rho bold u ) dV
Divergence theorem
{{partial %rho} over {partial t}} + nabla ( %rho bold u ) = 0
2) Momentum conservation. In an inertial reference frame the same fluid does not fill the same volume element for an extended interval dt. We must consider a volume co-moving with the fluid otherwise we cannot compute the effects of forces on the same mass element. No flux of mass in/out of the co-moving volume element. It follows the fluid lines
u
u
u
u
u
u
The momentum of the fluid in the volume V is:
int from{V} %rho( bold r,t ) bold u(bold r, t) dV

---
Forces acting on the fluid element changing the momentum:
1) Distance forces (gravity, electromagnetism…): The general form is
int from{V} %rho bold f dv
2) Contact forces: forces perpendicular to the volume element like Pressure (we neglect viscous forces).
int from{S} {-P} bold n dS
The equation for the momentum is finally:
d over {dt} int from{V} %rho bold u dV = int from{S} {-P} bold n dS + int from { V} %rho bold f dV
This equation is derived in a co-moving frame. How do we get back to an inertial reference frame where the variables depend on r and t? We use the material derivative!
Given any physical quantity f(r,t) of the fluid, ad example the temperature T(r,t), at a fixed point r in space the local derivative is:
{partial f ( bold u, t)} over {partial t }
If instead we move with the fluid, the variation of f will be given by the local variation + the variation due to the fluid motion. Ad example, in the case of stationary flux, the velocity does not depend on time locally, but as the fluid moves from a region of low cross section to a region of large cross section it changes.

---
Moving from S1 to S2 the local derivative of the velocity does not change (stationary fluid) but the derivative on a moving fluid element changes. The material derivative is the rate of change of a quantity (mass, temperature, pressurem energy, momentum..) as experienced by an observer that is moving along with the flow. The observations made by a moving observer are affected by the stationary time-rate-of-change of the property (∂f/∂t), but what is observed also depends on where the observer goes as it floats along with the flow (v·∇f).
alignl { partial bold u } over { partial t } = 0 ```````````````````````` color teal { stationary ```case} newline newline alignl { D bold u } over { D t } = bold u cdot nabla bold u
The gradient of a vector is a Jacobian or a 2nd order tensor. The divergence is the trace of this matrix.
bold nabla bold u = left ( matrix{{ partial u_x } over { partial x }# { partial u_x } over { partial y } # { partial u_x } over { partial z } ## { partial u_y } over { partial x }# { partial u_y } over { partial y } # { partial u_y } over { partial z } ## { partial u_z } over { partial x }# { partial u_z } over { partial y } # { partial u_z } over { partial z } } right )
In general for a fluid the material derivative is:
alignl { D bold u } over { D t } = { partial bold u } over { partial t } + bold u cdot nabla bold u
(bold u cdot nabla bold u )_x = u_x { partial u_x } over { partial x } + u_y { partial u_x } over { partial y } + u_z { partial u_x } over { partial z } newline (bold u cdot nabla bold u )_y= u_x { partial u_y } over { partial x } + u_y { partial u_y } over { partial y } + u_z { partial u_y } over { partial z } newline (bold u cdot nabla bold u )_z = u_x { partial u_z } over { partial x } + u_y { partial u_z } over { partial y } + u_z { partial u_z } over { partial z }
bold nabla bold u cdot bold u = left ( matrix{{ partial u_x } over { partial x }# { partial u_x } over { partial y } # { partial u_x } over { partial z } ## { partial u_y } over { partial x }# { partial u_y } over { partial y } # { partial u_y } over { partial z } ## { partial u_z } over { partial x }# { partial u_z } over { partial y } # { partial u_z } over { partial z } } right ) cdot left ( matrix { u_x## u_y ## u_z} right )

---
With the material derivative we can transform the equation for the momentum written for a moving fluid element to an equation written in a fixed reference frame with given coordinates.
{alignc d} over {dt} int from{V} {%rho bold u dV} = - int from{S}{ P } bold n dS + int from{V} {%rho bold f dV }
{alignc d} over {dt} int from{V} {%rho bold u dV} drarrow D over { Dt } int from{V} {%rho bold u dV} =int from{V} {D over { Dt }} ( {%rho bold u dV})= int from{V} {{D bold u} over { Dt }} %rho dV
The mass of the fluid element does not change with time so ρ dV is constant in time and the material derivative applies only to u
int from{V} {{D bold u} over { Dt }} %rho dV = int from{V} {%rho left ( { partial bold u } over { partial t } + bold u nabla bold u right ) dV}
int from{V} {%rho left ( { partial bold u } over { partial t } + bold u nabla bold u right ) dV} =int from{S} {-P} bold n dS + int from { V} %rho bold f dV = int from { V} left ( {-nabla P + %rho bold f } right ) dV
{%rho left ( { partial bold u } over { partial t } + bold u nabla bold u right )} = {-nabla P + %rho bold f }
3+1 equations for u + ρ but P is unknown. An additional equation is needed. For a gas, P is related to the density ρ and temperature T.
PV = nRT = m over M RT ````` drarrow ````` P = m over V {RT} over M = %rho {RT} over M

---
The relativistic formulation of Euler equations is more compact. Starting from the energy-momentum tensor (in normalized units i.e. c=1, otherwise ρ + p/c2) for a fluid:
Conservation of this tensor implies
T^{ %mu %nu } = ( %rho + p ) U^%mu U^%nu + p %eta^{ %mu %nu }
partial_%nu T^{ %mu %nu } = T^{%mu %nu}_{```````````` ,%nu} = 0
This equation translates back into Euler’s equations. Let’s see for example the first conservation equation. We adopt a non-relativistic limit
U^{ %mu} = ( 1, v^i) ```````` lline v^i rline << 1 ```````````p << %rho
partial_%nu T^{ %mu %nu } = partial_%nu (%rho + p) U^%mu U^%nu + (%rho+p) (U^%nu partial _%nu U^%mu + U^%mu partial_%nu U^%nu ) + partial_%nu p %eta^{%mu %nu} = 0
This equation can be contracted by multipling both members by
U_%mu
U_%mu partial_%nu T^{ %mu %nu } = partial_%nu (%rho + p) U_%mu U^%mu U^%nu + (%rho+p) newline ````````````````````````````````(U_%mu partial _%nu U^%mu U^%nu + U_%mu U^%mu partial_%nu U^%nu ) + U_%mu partial_%nu p %eta^{%mu %nu} = 0
Taking into account that
and that
U_%nu U^%nu =-1
U_%nu partial_%mu U^%nu = 1 over 2 partial_%mu (U_%nu U^%nu) = 1 over 2 partial_%mu (-1) = 0
since
alignl 1 over 2 partial_%mu (U_%nu U^%nu) = 1 over 2 ( U_%nu partial_%mu U^%nu + U^%nu partial_%mu ( %eta_{%nu %sigma} U^%sigma) ) = ``` newline `````````````````` 1 over 2 ( U_%nu partial_%mu U^%nu + %eta_{%nu %sigma} U^%nu partial_%mu U^%sigma ) = 1 over 2 ( U_%nu partial_%mu U^%nu + U_%nu partial_%mu U^%nu) = 2 1 over 2 U_%nu partial_%mu U^%nu
U_%nu partial_%mu T^{ %mu %nu } = -partial_%nu %rho U^%nu - partial_%nu p U^%nu - %rho partial_%nu U^%nu - p partial_%nu U^%nu + U^%nu partial_%nu p = `` newline `` - partial_%mu (%rho U^%mu) - p partial_%nu U^%nu approx color red { - partial_%nu (%rho U^%nu) = 0}
we get that
In non.relativistic limit.
partial_%nu (%rho U^%nu) = partial_t %rho + nabla (%rho bold v) = 0

---
The other equation comes from the projection of the derivative of T along a direction perpendicular to U. In GR the partial derivative must be changed to Covariant derivative.

---
Energy equation
D over { Dt} int from{V} left ( 1 over 2 bold u^2 +U right ) %rho dV = int from{V} %epsilon %rho dV - int from{S} bold F cdot bold n dS + int from{V} bold f cdot bold u %rho dV + int from{S} bold u cdot ( -P bold n ) dS
Where U is the internal energy, ε a local energy source and F the flux of energy from one region to another. In differential form the equation becomes
%rho D over { Dt} left ( 1 over 2 bold u^2 +U right ) = %epsilon %rho - nabla cdot bold F + %rho bold f cdot bold u - bold u cdot nabla P -P nabla cdot bold u
The ‘mechanical’ work is given by
bold u cdot %rho {D bold u} over {Dt} = bold u cdot ( - nabla P + %rho bold f ) drarrow newline %rho {D} over {Dt} left( 1 over 2 bold u^2 right) = - { } bold u cdot nabla P + %rho bold f cdot bold u
While the change in internal energy is given by:
%rho D over { Dt} U = %epsilon %rho - nabla cdot bold F - P nabla bold u
The thermal part related to gas compression is from the first principle
d U = - P dV + %delta Q

---
Application of Euler equations to an engineering case: the shape of the de Laval nozzle.
Derivation of Bernoulli’s equation for the case of a stationary (the fluid properties do not change with time) and inviscid fluid.
color red {If stationary} { partial bold u } over { partial t } = 0 ```````....```````` { partial %rho } over { partial t } = 0
alignl nabla ( %rho bold u ) = 0 newline {%rho left ( bold u nabla bold u right )} = {-nabla P + %rho bold f }
( bold u nabla ) bold u = nabla left ( 1 over 2 bold u^2 right ) - bold u times nabla times bold u
From calculus:
nabla left ( 1 over 2 bold u^2 right ) - bold u times nabla times bold u = {-{1 over %rho} nabla P + bold f }
We focus on a barotropic flow where the pressure is only function of the density P(ρ). We also introduce the state function enthalpy defined as:
h = int {dP over %rho } = int {dP over {d %rho } }{{d %rho} over %rho } `````` drarrow ``````` color red { dh = dP over %rho }
dP = left ( {partial P} over {partial x} right ) dx + left ( {partial P} over {partial y} right ) dy + left ( {partial P} over {partial z} right ) dz ``````````` drarrow ``````````` {nabla P} over %rho = nabla h
Introducing enthalpy in the previous equation, assuming that the force can be expressed as the gradient of a potential V, we get:
bold u times nabla times bold u = nabla left ({1 over 2 bold u^2} right ) + nabla h + nabla V = nabla left({1 over 2 bold u^2} + h + V right )

---
If we multiply both sides of the equation by u
bold u cdot left ( bold u times nabla times bold u right ) = 0 = bold u cdot nabla left({1 over 2 bold u^2} + h + V right )
The velocity u is tangent to the fluid motion, as a consequence the quantity
color red {{1 over 2 bold u^2} + h + V }
is constant along the streamlines. Bernoulli theorem!
Design of the nozzle: why the cross section is diverging when the flux becomes supersonic?

---
Let’s assume the flux through the nozzle is stationary and barotropic. We also neglect gravity (too small to significantly affect the high velocity gas). The cross section of the nozzle is called A(x) and it is measured at different section distant x from the top. The equations governing the flux are:
alignl 1 over 2 u^2 + h = const newline alignl %rho u A = const
The first equation is derived respect to x:
alignl 1 over 2 2 u {du} over {dx} + {dh} over {dx} = 0 ``````````drarrow ``````````````` u du + dh = 0 newline color green {alignl {dh} over {dx} = {dP} over {dx} cdot {1 over %rho} = {dP} over {d %rho} cdot { {d %rho} over {d x} }{ 1 over %rho}} newline alignl color blue { u cdot du + {1 over %rho} {{dP} over {d%rho}} d%rho = 0 }
The sound speed in barotropic approximation is:
c_s^2 = {dP} over {d %rho}

---
alignl color blue { u cdot du + {c_s^2 over %rho} d%rho = 0 } `````` drarrow ``````{ d %rho} over %rho = - { u^2 over c_s^2 } {{ du} over {alignc u }} = - M^2 {{ du} over {alignc u }}
Where M is the Mach number.
color magenta { alignl { d %rho} over %rho = - M^2 {{ du} over {alignc u }} } newline color magenta { alignl %rho u A = constant }
From the second equation we can derive the following relation between the differentials:
alignl 1 over { %rho u A } d over dx left( %rho u A right ) = { d %rho } over dx { uA } over { %rho u A } + { d u } over dx { %rho A } over { %rho u A } + { d A } over dx { u %rho } over { %rho u A } newline alignl { d %rho } over { %rho} + { d u } over {alignc u} + { d A } over {alignc A} = 0 ```````drarrow ``````` { d %rho } over {alignc %rho} = - {{ d u } over {alignc u} } - { d A } over {alignc A}
Combining the equations we finally get to:
color red { alignl - {{ d A} over {alignc A} } = (1 - M^2) {{ du} over {alignc u }} }
If M <<1 (subsonic flow), A must be reduced to increase u
If M > 1 (supersonic flow) A must be increased to increase u
The optimal design of the nozzle has to converge the flux until the velocity becomes supersonic. From then on, the nozzle has to be divergent.

---
alignl color blue { u cdot du + {c_s^2 over %rho} d%rho = 0 } `````` drarrow ``````{ d %rho} over %rho = - { u^2 over c_s^2 } {{ du} over {alignc u }} = - M^2 {{ du} over {alignc u }}
Where M is the Mach number.
color magenta { alignl { d %rho} over %rho = - M^2 {{ du} over {alignc u }} } newline color magenta { alignl %rho u A = constant }
From the second equation we can derive the following relation between the differentials:
alignl 1 over { %rho u A } d over dx left( %rho u A right ) = { d %rho } over dx { uA } over { %rho u A } + { d u } over dx { %rho A } over { %rho u A } + { d A } over dx { u %rho } over { %rho u A } newline alignl { d %rho } over { %rho} + { d u } over {alignc u} + { d A } over {alignc A} = 0 ```````drarrow ``````` { d %rho } over {alignc %rho} = - {{ d u } over {alignc u} } - { d A } over {alignc A}
Combining the equations we finally get to:
color red { alignl - {{ d A} over {alignc A} } = (1 - M^2) {{ du} over {alignc u }} }
If M <<1 (subsonic flow), A must be reduced to increase u
If M > 1 (supersonic flow) A must be increased to increase u
The optimal design of the nozzle has to converge the flux until the velocity becomes supersonic. From then on, the nozzle has to be divergent.

---
Parker’s solution for an unmagnetized solar wind
Simplifications: spherically symmetric, isothermal and non-magnetic non-rotating flux.
The steady state equation for the radial component of the momentum is:
%rho u { du } over { dr } = - {{ dP } over { dr }} - %rho {G M} over r^2
Isothermal approximation →
{ dP } over { dr } = {{ dP } over { d %rho }} {{ d%rho } over { d r }} = c_s^2 {{ d%rho } over { d r }}
u { du } over { dr } = - c_s^2 {{ d %rho } over { dr }} 1 over %rho - {G M} over r^2
From the mass conservation equation
{ d %rho } over {dr} 1 over {alignc %rho} = - {{ d u } over { dr } 1 over {alignc u} } - { d A } over { dr } 1 over {alignc A}
It is a symmetrical spherical flux so the area is 4πr2
c_s^2 { d %rho } over {dr} 1 over {alignc %rho} = -c_s^2 {{ d u } over { dr } 1 over {alignc u} } - {2 c_s^2 } 1 over {r}
u { du } over { dr } = c_s^2 {{ d u } over { dr } 1 over {alignc u} } + {2 c_s^2 } over r - {G M} over r^2
u^2 over u { du } over { dr } - c_s^2 {{ d u } over { dr } 1 over {alignc u} } = {{2 c_s^2} over r }- {G M} over r^2 ```````` drarrow `````` newline newline ( u^2 - c_s^2) over u { du } over { dr } = {2 c_s^2 } over r - {G M} over r^2

---
The equation is similar to that of de Laval nozzle. The solution can be written as (C is an integration constant):
left ( u over c_s right)^2 - ln left ( u over c_s right)^2 = 4 ln left ( r over r_c right) + { 4 r_c } over r + C ````````where ``````r_c = { GM } over 2 c_s^2
Solution V has C=-3
At the critical point the flux from subsonic becomes supersonic (as in the nozzle) and vc = cs

---
Accretion disks
Cylindrical coordinates are typically used:
(r,%phi,z)
The disk is considered thin and axis-symmetric
partial over { partial %phi } = 0 newline bold u cdot bold e_z = 0
The fluid velocity is
bold u = ( u, r %OMEGA, 0 )
In cylindrical coordinates the r-component of the momentum equation is
{partial u } over {partial t} + u {partial u } over {partial r} - r %OMEGA^2 = - {1 over %rho} { {partial P} over {partial r} } - {partial %PSI} over {partial r}
Where the gravitational potential is
%PSI = - { {GM } over { (r^2 + z^2)^{1/2} }}
{partial P} over {partial r} <<1 ```````````u=0
Under the simplification conditions that
r %OMEGA^2 = { {GM } over { r^2 }} `````````drarrow `````````````` %OMEGA = sqrt { {GM} over r^3 }
The usual Keplerian rotation.

---
1) Euler equation for u in cylindrical coordinates.
Vectorial form
%rho {{ D vec u } over { Dt }} = - nabla P - %rho nabla %PSI
r-component
%rho ( {partial u_r } over {partial t} + u_r {partial u_r } over {partial r} + {u_%phi} over {r} {partial u_r } over {partial %phi} -{{u_%phi^2} over r} + u_z {partial u_r } over {partial z}) = -{ {partial P} over {partial r} } - %rho {partial %PSI} over {partial r}
φ-component
%rho ( {partial u_%phi } over {partial t} + u_r {partial u_%phi } over {partial r} + {u_%phi} over {r} {partial u_%phi } over {partial %phi} + {{u_%phi u_r } over r} + u_z {partial u_%phi } over {partial z}) = - {{1} over {r}} { {partial P} over {partial %phi} } - %rho { partial %PSI} over { partial %phi }
z-component
%rho ( {partial u_z } over {partial t} + u_r {partial u_z } over {partial r} + {u_%phi} over {r} {partial u_z } over {partial %phi} + u_z {partial u_z } over {partial z}) = - { {partial P} over {partial z} } - %rho { partial %PSI} over { partial z }

---
2) Scale height of a disk in isothermal approximation
In hydrostatic equilibrium, uz = 0 so the z-component of the Euler equations read:
1 over %rho { {partial P} over {partial z} } = - { { partial %PSI} over { partial z }} = partial over {partial z} left [ {GM} over {(r^2 + z^2)^{1/2}} right ] sim - {{GM z } over {r^3}}
In isothermal approximation (fixed temperature profile), the state equation is:
P = { R %rho T } over %mu
c_s^2 = {dP} over {d %rho} = {RT} over %mu `````````%mu `is`the`mean`molecular`weight
1 over %rho { {partial P} over {partial z} } = {1 over %rho} {c_s}^2 { {partial %rho} over {partial z} } = - {{GM z } over {r^3}} ```````` drarrow `````` ln ( %rho ) = - {1 over 2} { {%OMEGA}^2 over {c_s^2} } z^2
%rho (z ) = e^{ - {1 over 2} { {%OMEGA}^2 over {c_s^2} } z^2} = e^{ - {1 over 2} z^2 over H^2} `````````where ```````` H = { c_s over {%OMEGA}}
H = c_s over %OMEGA = c_s over { %OMEGA r } r = h r
The vertical disk scale-height h is around 0.05 so the isothermal sound speed is smaller than the keplerian velocity

---
3) Equation for the superficial density of a disk
%SIGMA( r,t) = int from{ - infinity } to{ infinity } %rho (r,t,z) dz ``````` drarrow ``````` %SIGMA = %rho_0 sqrt{ 2 %pi } ``h
Shear `` ``````` A = r { {d %OMEGA} over {dr} } = - {3 over 2} sqrt( GM) r^{-5/2}
Specific angular momentum (per unit of mass)
vec J = r cdot vec e_%phi cdot vec u = r left lbrace stack{0 # 1 # 0} right rbrace cdot left lbrace stack{u # r %OMEGA # 0} right rbrace = r^2 %OMEGA = r u_{ %phi }
The %phi component of the momentum conservation equation
must include a viscosity term
%rho left lbrace { partial u_%phi } over { partial t } + u { partial u_%phi } over { partial r } + { u u_%phi } over { r } right rbrace = f_%phi %rho
where`` f is the viscous force per mass unit
{partial J} over { partial t} + u {partial J} over {partial r } = { DJ} over {Dt} = r f_%phi
u { partial j} over {partial r } = u { partial(r u_%phi) } over { partial r} = u u_%phi + u r {partial u_{%phi }} over { partial r }

---
4)
4) Viscosity
Friction between adiacent surfaces. The component of viscosity tangent to the motion is
%mu A( r ) = %rho %nu A( r )
This is a force per unit length. The larger is the shear or the gas density, the higher is the viscosity
Let’s consider a ring of gas with width dr. It feels the friction from the gas at the outer and inner edges of the ring.
r
dr
The force at the inner edge tends to accelerate it while that at the outer edge slows it down due to the Keplerian motion.
F_{inn} = 2 %pi [ r %nu lline A rline int from{- infinity } to{ infinity } %rho dx ]_{ r - dr/2 } = 2 %pi ( r %nu lline A rline %SIGMA )_{ r -dr/2 }
F_{out} = 2 %pi ( r %nu lline A rline %SIGMA )_{ r + dr/2 }
The torque acting on the ring, assuming that the forces act at center of the ring r, is
Be careful!, the sign of d Ω /dt is negative.
T = F_{inn} r_{inn} - F_{out} r_{out}

---
5)
T = - 2 %pi (r^2 %nu %SIGMA r {d %OMEGA } over {dr} )_{ r - dr/2 } + 2 %pi (r^2 %nu %SIGMA r {d %OMEGA } over {dr} )_{ r + dr/2 } = ```
``` = 2 %pi {d} over {dr} (r^2 %nu %SIGMA r {d %OMEGA } over {dr} ) cdot dr
M_{ring} = 2 %pi r %SIGMA dr
The ring mass is:
T for mass unit is
T = r f_{%phi} = 2 %pi {d} over {dr } (r^3 %nu %SIGMA {d %OMEGA } over {dr} ) {dr } over {2 %pi r %SIGMA dr} = ```
``` = {1} over {r %SIGMA } {d} over {dr } (r^3 %nu %SIGMA {d %OMEGA } over {dr} )
The equation for the specific angular momentum is finally:
{DJ} over {dt} = {1} over {r %SIGMA } {d} over {dr } (r^3 %nu %SIGMA {d %OMEGA } over { dr} )

---
6)
From the mass conservation we can derive an additional equation:
Which, once integrated in z, gives an equation for the superficial density Σ
{D %rho} over {Dt } + %rho nabla cdot vec u =0
{D %SIGMA} over {Dt } + %SIGMA nabla cdot vec u = { partial %SIGMA} over {partial t} + nabla cdot (u cdot %SIGMA ) = 0
In cylindrical coordinates
%SIGMA nabla cdot vec u = {1} over {r} %SIGMA {partial} over {partial r} ( r u ) + {1} over {r} %SIGMA {partial u_{%phi}} over {partial %phi} + %SIGMA {partial u_{z}} over {partial z} ```````````````````` u nabla %SIGMA = 1 over r u partial over { partial r} ( r %SIGMA )
The last two terms are =0 because of the axisymmetric and thin disk approximations.
{partial %SIGMA} over {partial t} + {1} over {r} {partial} over {partial r} ( r u %SIGMA) = 0
The Keplerian frequency Ω is function only of r and so is also J by definition
J = r^2 %OMEGA
{DJ} over {Dt } = {dJ} over {dr} cdot u
Where u is the component along r of the fluid velocity vector u. We are looking for a stationary solution for J → its time partial derivative = 0

---
7)
{DJ} over {dt} = {1} over {r %SIGMA } {d} over {dr } (r^3 %nu %SIGMA {d %OMEGA } over { dr} )
J = r^2 %OMEGA
{DJ} over {Dt } = {dJ} over {dr} cdot u
%OMEGA = sqrt{ {GM} over {r^3} }
{partial %SIGMA} over {partial t} + {1} over {r} {partial} over {partial r} ( r u %SIGMA) = 0
u {dJ} over {dr} = {1} over {r %SIGMA } {d} over {dr } (r^3 %nu %SIGMA {d %OMEGA } over { dr} )
u r %SIGMA = {1} over { {dJ} over {dr} } {d} over {dr } (r^3 %nu %SIGMA {d %OMEGA } over { dr} )
{partial %SIGMA} over {partial t} + {1} over {r} {partial} over {partial r } ( ({dJ} over {dr})^{-1} {d} over {dr} (r^3 %nu %SIGMA {d %OMEGA } over { dr} ) ) = 0
{partial %SIGMA} over {partial t} + {1} over {r} {partial} over {partial r } ( ({d(r^2 %OMEGA)} over {dr})^{-1} {d} over {dr} (r^3 %nu %SIGMA {d %OMEGA } over { dr} ) ) = 0
{partial %SIGMA} over {partial t} = {3} over {r} {partial} over {partial r } ( r^{1/2} {partial} over {partial r} [ %nu %SIGMA r^{1/2} ] )
{partial %SIGMA} over {partial t} = {3} over {r} {partial} over {partial r } ( r^{1/2} {partial} over {partial r } [ %nu %SIGMA r^{1/2}])

---
8)
5) Viscous mass accretion rate on the star:
The conservation of mass in an annulus leads to:
{partial %SIGMA} over {partial t} + {1} over {r} {partial} over {partial r} ( r u %SIGMA) = 0 ```` drarrow ```` 2 %pi r {partial %SIGMA} over {partial t} = 2 %pi {partial} over {partial r} ( - r u %SIGMA)
For the angular momentum:
L = r v_{%phi} M = r cdot (r %OMEGA) cdot (2 %pi r dr %SIGMA )
F_L = (r M v_%theta dr) 1 over dt = r M v_%theta cdot u
 Since we get (u is negative )
alignl {partial } over {partial t} ( 2 %pi r dr %SIGMA cdot r^2 %OMEGA ) = - 2 %pi (r +dr) u(r+dr) %SIGMA(r+dr) (r+dr)^2%OMEGA(r+dr) `` newline + 2 %pi r u(r) %SIGMA(r) r^2 %OMEGA(r) newline newline alignl 2 %pi r dr {partial } over {partial t} ( %SIGMA cdot r^2 %OMEGA )= - 2 %pi { {partial} over {partial r } } {( r %SIGMA u cdot r^2 %OMEGA )} dr
In the change of angular momentum due to the mass flux between adjacent rings also the viscous force contributes.
See pg. 5 without division by the mass.
2 %pi r {partial } over {partial t} (%SIGMA cdot (r^2 %OMEGA) ) + 2 %pi {partial} over {partial r } ( r %SIGMA u cdot r^2 %OMEGA ) = ```
``` = 2 %pi {partial} over {partial r} ( r^2 %nu %SIGMA r {d %OMEGA} over {dr} )
We look for a stationary solution to the differential equation where Σ is constant with time.
{partial} over {partial t} drarrow 0

---
9)
{partial} over {partial r } ( r %SIGMA u cdot r^2 %OMEGA ) = {partial} over {partial r} ( r^2 %nu %SIGMA r {d %OMEGA} over {dr} )
The mass accretion rate from a ring to an inner one is given by:
- {{partial} over {partial r } ( dot M r^2 %OMEGA ) } = {partial} over {partial r} ( 2 %pi %nu %SIGMA r^3 {d %OMEGA} over {dr} )
˙
=
−
π
Σ
/
=
−
π
Σ
Integrating in r the previous equation we get:
- int from{r_s} to{r} { partial over {partial r} left ( dot M (r') r'^2 %OMEGA (r') right ) dr'} = int from{r_s} to{r} {partial over {partial r} left ( 2 %pi %nu %SIGMA (r') r'^3 {d %OMEGA (r')} over {dr'} right ) dr' }
Where rs is the star radius. It is assumed for simplicity that the inner limit of the disk is the star surface. In this case:
- dot M r^2 %OMEGA = 2 %pi %nu %SIGMA r^3 {d %OMEGA} over {dr} + const
In the constant all values are computed on the star surface where
{d %OMEGA} over {dr} =0
..since the star rotates as a rigid body (approx…).
const = - dot M r_s^2 %OMEGA (r_s)

---
10)
At the end
dot M r^2 sqrt( GM over r^3 ) = - 2 %pi %SIGMA %nu 3 over 2 r^2 sqrt( GM over r^3 ) + dot M r_s^2 sqrt( GM over r_s^3 ) = ``newline - 3 %pi %SIGMA %nu r^2 sqrt( GM over r^3 ) + dot M sqrt(r_s over r) sqrt( GM over r^3 ) r^2
dot M (1 - sqrt( {r_s} over {r} )) = 3 %pi %nu %SIGMA
For r >> rs (in the majority of the disk apart very close to the inner border) the following is obtained:
dot M = 3 %pi %nu %SIGMA
This value is derived assuming a stationary state, however in general Σ depends on t.
The Shakura-Sunayev alpha viscosity:
%nu = %alpha c_s h
Alpha is a constant all over the disk and an adimensional quantiy. It ranges from 0.1 to 0.00001.

---
Observations suggest that the mass accretion rate depends on the mass of the central object. It implies that the heavier is the star the more massive is the disk (higher Σ).
dot M = 3 %pi %nu %SIGMA

---
6) Self-similar solutions:
11)
When
%nu infinity r^{ %gamma }
{partial %SIGMA} over {partial t} = {3} over {r} {partial} over {partial r } ( r^{1/2} {partial} over {partial r } [ %nu %SIGMA r^{1/2}])
The equation
admits self-similar solutions of the type:
%SIGMA(r,t) = {C} over {3 %pi %nu_1 r^%gamma } T^{ {-({5} over {2} -%gamma)} / {(2 - %gamma)} } exp( -bar r {(2- %gamma)} over {T} )
T = {t} over {t_s} +1 ````` dove ````` t_s = {1} over {3 (2 - %gamma)^2} {R_1} over {%nu_1 } ```````````` color teal { %nu = %alpha c_s h ```[1/s]}
ts is the viscous scaling time: for timescales shorter than ts the system does not significantly evolve.
bar r = {r} over {R_1} ````` e ````` %nu_1 = %nu( R_1 )
where R1 is a radial scaling factor (1 AU etc…). The constant C is given from the initial conditions.
Self-similar: it means that they are scalable and do not depend on the initial conditions.

---
12)
dot M(r,t) = C T^{ {- ({5} over {2} -%gamma)} / {(2 - %gamma)} } exp( -bar r {(2- %gamma)} over {T} ) [ 1 - {2 (2- %gamma)r^{(2-%gamma)}} over T ]
When ``````` r = r_T = R_1 [T over {2 (2 - %gamma)} ] ^{1 over {(2 - %gamma)}}
The mass accretion rate changes sign: positive inside, negative outside.
PROBLEM WITH ACCRETION DISKS: the rate of viscous dissipation is too slow! In addition, from observations it looks like disks are not expanding….

---
Ages of disks estimated in stellar clusters: fraction of stars with disks as a function of the cluster age. However, these ages might be too short since clusters dissipate and only core stars are observed for older clusters. .
..these stars are strongly irradiated by O, B bright stars which form in the core of clusters. For these reason, core stars lose their disks on a shorter timescale. The disk age is then underestimated. Red line more realistic estimate. (Pfalzner et al 2014).

---
7) Vertical structure of the disk.
T ~ 104
8) Boundary layer (border between the star surface and the disk)

---
13)
9) Photoevaporation
{partial} over {partial t} %SIGMA + {1} over {r} {partial } over {partial r} (r %SIGMA u_r) = -dot %SIGMA_{ pe }
At a given radius (about 1-10 au) the mass inflow due to viscosity is slower than the mass loss due to photoevaporation. The inner disk is not refilled and a hole developes in the inner region which propagates outside.

---
Transition disks.
Planet formation? Stellar winds? Photoevaporation?

---
10) Self gravity
Q = { c_s %OMEGA_K} over { %pi G %SIGMA }
Toomre parameter

---
Planet formation by disk gravitational instability. Only giant planets without a solid core. They form in the outer parts of the disk where the temperature is lower allowing gravitational instability.

---
Sound waves in a fluid:
alignl {partial %rho} over { partial t} + nabla (%rho bold u) = 0 newline alignl {partial bold u} over { partial t} + bold u nabla bold u = - { 1 over %rho } nabla P
We apply a small perturbation to the stationary fluid with ρ0, P0 and u0 = 0.
P = P_0 + %DELTA P `````` %rho = %rho_0 + %DELTA %rho ``````` bold u = bold u_0 + %DELTA bold u
alignl {partial (%rho_0 + %DELTA %rho) } over { alignc partial t} + nabla ((%rho_0 + %DELTA %rho)(bold u_0 + %DELTA bold u)) = 0 drarrow newline newline alignl {partial %DELTA %rho } over { alignc partial t} + %rho_0 nabla (%DELTA bold u) = 0
ρ0 can be taken out of the nabla since it is constant.
alignl {partial (bold u_0 + %DELTA bold u) } over { alignc partial t} + (bold u_0 + %DELTA bold u) nabla (bold u_0 + %DELTA bold u) = -{{ alignc 1} over { (%rho_0 + %DELTA %rho)}} (P_0 + %DELTA P) drarrow newline alignl {partial %DELTA bold u } over { alignc partial t} + %DELTA bold u nabla (%DELTA bold u) = -{ 1 over { %rho_0}} nabla (%DELTA P) drarrow newline newline alignl {partial %DELTA bold u } over { alignc partial t} = -{ 1 over { %rho_0}} nabla(%DELTA P)
Neglecting 2nd order terms in Δu

---
Assuming a barotropic flux with P(ρ) we get:
alignl nabla ( %DELTA P) = nabla ({dP} over {d%rho} %DELTA %rho ) = {dP} over {d%rho} nabla ( %DELTA %rho ) newline newline newline alignl {partial %DELTA bold u } over { alignc partial t} = -{ 1 over { %rho_0}} {dP} over {d %rho} nabla(%DELTA %rho)
Both P and ρ are constants so the derivative is constant.
1st equation derived respect to t, third multiplied by
alignl partial over {partial t} left ({alignl {partial %DELTA %rho }} over { alignc partial t} right ) + partial over {partial t} left ( %rho_0 nabla (%DELTA bold u) right ) = 0 newline newline alignl - %rho_0 nabla left( {partial %DELTA bold u} over {alignc partial t} right ) = - %rho_0 nabla left( - { 1 over %rho_0 } {dP} over {d %rho} nabla (%DELTA %rho) right )
%rho_0 nabla
Since we can exchange the derivative order in the first term of last equation
%rho_0 nabla left ({partial %DELTA bold u} over { partial t} right ) = partial over {partial t} left ( %rho_0 nabla (%DELTA bold u) right )
We can combine the two equations in a single wave equation
partial^2 over {partial t^2 } %DELTA %rho = {dP} over {d%rho} nabla^2 (%DELTA %rho)

---
The solution of the wave equation is a perturbation of the form:
alignl %DELTA %rho = %DELTA %rho_0 e^{ i(bold k cdot bold x - %omega cdot t) }
Inserting this solution in the wave equation we get
alignl %DELTA %rho_0 (i %omega)^2 = {dP} over {d %rho} (i bold k)^2 %DELTA %rho_0
...and then the dispersion relation
{dP} over {d %rho} = %omega^2 over k^2=c_s
...where cs is the propagation speed of signals in the fluid (sound speed).

---
T^{00} = 1 over c^2 ( 1over 2 %epsilon_0 E^2 + 1 over {%mu_0} B^2)
EM field, 00 component
T^{%mu %nu } = E over c^2 {( U^%mu U^%nu)} over %gamma^2 %delta( bold x - bold x_p )
For single particle