CAPITOLO 9
ORBITAL ELEMENTS
- Relative motion
- Kepler’s equation
- Transformation from orbital elements to cartesian coordinates and viceversa.

---
Relative motion equation for 2 bodies
vec F_1
m_1
vec F_2
vec r
m_2
vec r_1
vec r_2
vec r_1 + vec r = vec r_2 newline vec r = vec r_2 - vec r_1
O
vec F_1= {G m_1 m_2} over r^3 vec r = m_1 vec ddot r_1 ````` Force `` on `` m_1 newline vec F_2 = -{{G m_1 m_2} over r^3 } vec r = m_2 vec ddot r_2 ````` Force `` on ``m_2
alignl m_1 vec ddot r_1 + m_2 vec ddot r_2 = {vec {a}}_{ cm} = 0 `````````` No``external``forces. newline newline alignl color red { vec ddot r} = vec ddot r_2 - vec ddot r_1 = left ( - {{G m_1 m_2} over {alignc r^3 m_2 }} - {{G m_1 m_2} over {alignc r^3 m_1}} right ) vec r = color red { - {{G (m_1 + m_2)} over {alignc r^3 }} vec r }

---
Orbital elements: definition
color blue { { d^2 vec r } over dt^2 + %mu vec r over r^3 =0 }
Relative motion equation:
color green{ %mu = G(m_1 + m_2)}
The system is isolated, so 3-1 degree of freedom. This implies that the motion occurs on a 2D plane.
Integral of motion: angular momentum
color blue { vec h = vec r times vec dot r }
The relative equation of motion in polar coordinates reads
color blue { vec ddot r= (ddot r - r dot %theta^2 ) hat r + left [ 1 over r d over dt (r^2 dot %theta) right] hat %theta }
hat r, hat %theta
Splitting the equation along the two versors
alignl (ddot r - r dot %theta^2 ) hat r + %mu r over r^3 = 0 ``````````` drarrow `````` hat r newline alignl 1 over r d over dt (r^2 dot %theta) = 0 `````````` drarrow ````` hat %theta
color blue { vec h = r hat r times (dot r hat r + r dot %theta hat %theta) = 0 + r^2 dot %theta hat z } ``````````````` color red { Constant}

---
Solution of the two body equation of motion: trajectory
color blue {trajectory: ````` r(%theta) }
color red {( ddot r - r dot %theta^2) + %mu over r^2 = 0 }
color green {Auxiliary variable ````` y = 1 over r }
dot r = - {1 over y^2} dot y = - {1 over y^2} {dy} over {d %theta} dot %theta = r^2 dot %theta {dy} over {d %theta} =- h {dy} over {d %theta } newline ddot r = -h d over {dt} left ( {d y} over {d %theta} right ) = -h {d^2 y} over {d %theta^2} dot %theta= - h^2 y^2 {d^2 y} over {d %theta^2}
- h^2 y^2 {d^2 y} over {d %theta ^2 } - h^2 y^3 + %mu y^2 = 0
Differential equation with constant coefficients
color green { {d^2 y} over {d %theta ^2 } + y = %mu over h^2 }
color green { y(%theta) = %mu over h^2 ( 1 + e cos(%theta - %theta_0) ) }
color red { r(%theta) = p over { 1 + e cos(%theta - %theta_0)} } `````````````````````` color blue { p = h^2 over %mu }

---
Ellipse: `````` p = a( 1 - e^2 ) ````````e < 1
h^2 over %mu = a ( 1 - e^2) `````` drarrow ````` newline newline color red {h = sqrt {%mu a (1-e^2)}}
Parabola: `````` p = 2 q ````````q ``min `` dist ``` newline alignl e=1
Hyperbola: `````` p = a ( e^2 -1 ) ```` e > 1

---
Elliptical motion in more details:
a e
a (1 - e^2)
Focus
Pericenter distance a(1-e)
b = a sqrt (1 - e^2) newline semiminor `` axis
tilde %omega ``````````` drarrow ````````` color blue {pericenter longitude}
Area = %pi a b newline Perimeter = 4 %pi E( e )
alignl E( e ) = int from{0} to{%pi over 2} sqrt( 1 - e^2 sin^2 %theta ) d %theta newline alignl complete `` elliptical `` integral `` of `` the `` 2^nd `` kind
Pericenter
Apocenter

---
Time dependence
color blue {V_{ar} = h over 2 ```````` drarrow ```````` V_{ar} cdot T = { hT } over 2 = %pi a b = %pi a^2 sqrt(1 - e^2) } ```````` newline color red {h = sqrt( %mu a (1 - e^2 )) } ```````` drarrow `````` h^2 over %mu = a( 1-e^2 )
alignl T = 2 %pi sqrt( a^3 over %mu ) `````````````` Periodo newline alignl color red {n = {2%pi } over T = sqrt {%mu over a^3} = sqrt{ {G (m_1 + m_2 )} over { alignc a^3} } `````````````Mean `` motion }
M = n (t -t0) Mean Anomaly f=θ True anomaly
Average angle determining the exact position only in the case of circular motion.
Energy integral: second constant of motion:
vec dot r cdot vec ddot r + %mu vec dot r cdot vec r over r^3 = 0 newline d over { dt } left ( { vec dot r cdot vec dot r} over 2 - %mu over r right )
color blue {1 over 2 v^2 - %mu over r = C } = color red { -{ %mu over {2a} }}
The system has 2 integrals of motion:
Angular momentum (relative motion) h
Energy (relative motion) E
3-2 = 1 degree of freedom

---
Kepler equation: full time dependence
Q
Q
U is the eccentric anomaly
P
GOAL: compute r,f as a function of U and then derive a time equation for U
f
R
alignl FR = r cos f = a cos U - ae newline alignl PR = r sin f = sqrt { 1-e^2} a sin U
alignl r = a(1 - e cos U) newline newline alignl tg left ( f over 2 right ) = left ( {1+e} over {1-e} right )^{ 1 over 2 } tg left ( U over 2 right )
color green { tg left ( f over 2 right ) `````````````` drarrow `````````````````````` cos f = 1 - 2 sin^2 f over 2 ```````` r cos f = r left ( 1 - 2 sin^2 f over 2 right ) } newline color green { 2 r sin^2 f over 2 = r - r cos f = a ( 1 - e cosU) - a cos U + ae = a ( 1+e) (1 -cosU ) } newline color green { cos f = 2 cos^2 f over 2 -1 ```````` 2 r cos^2 f over 2 = a ( 1-e)(1+cos U ) }

---
How to compute U as a function ot t?
color blue {%mu left ( 2 over r - 1 over a right ) = v^2 = dot r^2 + ( r dot f)^2 } ``````````````````````since ``````` {E = - {%mu over {2a} }}
alignl dot r = { na} over {sqrt {1 - e^2} } newline alignl r dot f = { na} over {sqrt {1 - e^2} } ( 1 + e cos f )
From Murray & Dermott, pg 31
alignl color blue {dot r = { na} over r sqrt {a^2 e^2 - (r-a)^2} = { n a^2 e sin U } over { a(1-e cos U) } } newline alignl color blue { dot r = a e sin U dU over dt }
color magenta {dU over dt = n over { (1-e cosU) }}
U - e sin U = M = n ( t-t_0 )
Kepler equation: it gives the solution for the time evolution along the trajectory r(θ).

---
Iterative solution of Kepler equation (for low eccentricity orbits).
U_0 = M newline U_1 = U_0 + e sin U_0 newline U_2 = U_0 + e sin U_1 newline ...... newline ...... newline U_{ i+1 } = U_0 + e sin U_i
For high eccentricity orbits, Newton-Raphson method grants faster convergence.
alignl f(U) = U - e sin U - M= 0 newline alignl f'( U) = 1 -e cos U > 0 ```````` single ``solution
alignl U_0 = U newline color blue {alignl f( U_0+ %delta) = f(U_0) + f'(U_0) cdot %delta + ...=0 } newline alignl U_1 = U_0 + %delta ```````` color red {%delta = - {{f(U_0)} over {f'(U_0)}} }newline alignl ................. newline alignl U_{i+1 } = U_i + %delta = U_i - {{f(U_i)} over {f'(U_i)}}
Quadratic convergence, much faster than the iterative method

---
Hohmann transfer: it uses the lowest possible amount of energy in transferring probe from circular orbit of radius r1 to circular orbit of radius r2.
alignl a(1-e) = r_1 newline alignl a(1+e) = r_2 newline alignl a (1-e)+a(1+e) = 2a= r_1 + r_2 newline alignl color blue {a = {r_1 + r_2} over 2 `````````````````````` e = 1 - r_1 over a }
Computation of the Δv needed to perform the orbital transfers.
1 over 2 v^2 -%mu over r = - {%mu over { 2a} } ```` drarrow v^2 = ( 2over r - 1 over a ) %mu newline color blue {v = sqrt{ %mu left ( 2 over r - 1 over a right ) }}

---
alignl color green {v_{C1} = sqrt{ %mu left ( 2 over r - 1 over a right ) } = sqrt {%mu over r_1} ``````````````````````` V_{ C2 } = sqrt {%mu over r_2} } newline alignl color magenta { V_{PT} = sqrt { %mu left( alignc 2 over {a(1-e)} right ) - 1 over a} = sqrt { %mu over a left( {(1+e)} over {(1-e)} right )} ``````````````````````` V_{AT} = sqrt { %mu over a left( {(1-e)} over {(1+e)} right )} }
alignl color blue {%DELTA v_1 = V_{PT} - v_{C1} = sqrt { %mu over a left( {(1+e)} over {(1-e)} right ) } - sqrt { %mu over r_1} } newline alignl color blue { %DELTA v_2 = v_{C2}- V_{AT} = sqrt { %mu over r_2} - sqrt { %mu over a left( {(1-e)} over {(1+e)} right )} }
Flight transfer time is equal to half the period of the transfer orbit
T_{ of} = %pi sqrt {a^3 over %mu}

---
Transformation from orbital elements to cartesian coordinates and viceversa: the planar case
bold {size 15 { color red { a,e,M ````drarrow ``` vec x, vec v } }}
alignl color blue { U - e sin U = M ``````` M ``` drarrow ``` U } newline alignl color maroon {alignl r= a( 1-e cosU ) ```````````` tg left( f over 2 right ) = left( {1+e} over {1-e} right )^{ 1over 2 } tg left( U over 2 right ) ``````drarrow ```` r,f } newline color purple { alignl size 15 {color red {x }} = r cos f = a (cos U -e) ``````` size 15 {color red { y}} = r sin f = a sqrt( 1-e^2 ) sin U } newline alignl color green { size 15 {color red {v_x}} = -{ {na sin U } over { 1 - e cos U} } `````` size 15 {color red {v_y}} = { {na sqrt(1-e^2) cos U } over { 1 - e cos U} } }
dU over dt = n over { 1 - e cos U }
bold {size 15 { color red { vec x, vec v ````drarrow ``` a,e,M } }}
alignl color blue { r = sqrt(x^2 + y^2 + z^2) ``````` v=sqrt(v_x^2 + v_y^2 + v_z^2) } newline alignl color maroon {C = 1 over 2 v^2 - %mu over r = - {%mu over {2 size 15 {color red { a}}} }} newline alignl color purple { h = abs{r times v} = sqrt {%mu a (1- size 15 {color red { e^2}}) } } newline alignl color green { r = {a (1 - e^2) } over { 1 + e cos size 15 {color red { f}}} ``````` dot r = {n a e sin size 15 {color red { f }}} over {sqrt (1 - e^2)} = {vec v cdot vec r} over {alignc r } } newline alignl color magenta {tg left( f over 2 right ) = left( {1+e} over {1-e} right )^{ 1over 2 } tg left( U over 2 right ) ````````` U -e sin U = size 15 {color red { M}} }

---
Elliptical orbit in 3D

---
M_3 = left langle matrix{cos %omega # - sin %omega # 0 ## sin %omega # cos %omega # 0 ## 0#0#1 } right rangle
1) Rotation around z-axis by an angle ω (pericenter argument)
M_1 = left langle matrix{1 # 0 # 0 ## 0 # cos i # -sin i ## 0# sin i #cos i } right rangle
2) Rotation around x-axis by an angle i (inclination)
M_3 = left langle matrix{cos %OMEGA # - sin %OMEGA # 0 ## sin %OMEGA # cos %OMEGA # 0 ## 0#0#1 } right rangle
2) Rotation around z-axis by an angle Ω (node longitude)
alignl left ( stack{X # Y # Z} right ) = M_3 M_1 M_3 left ( stack{r cos f # r sin f # 0} right ) = ````` newline ```` newline ````newline ````````````````````````````````````left ( stack {r cos %OMEGA cos (%omega +f) - r sin %OMEGA sin (%omega +f) cos i # r sin %OMEGA cos (%omega +f) + r cos %OMEGA sin (%omega +f) cos i # r sin (%omega +f) sin i } right )

---
Baricentric orbits.
B
m2
m1
x1
x

---
Baricenter position in the baricenter reference frame.
alignl -m_1 x_1 + m_2 ( x-x_1) = 0 drarrow
R_1 = m_2 over { m_1 + m_2 } R newline R_2 = m_1 over { m_1 + m_2 } R
x_1 = m_2 over { m_1 + m_2 } x `````````drarrow
R1 and R2 are the radial distance from the baricenter of the bodies 1 and 2.
R_1^2 dot %theta = left ( m_2 over { m_1 + m_2 } right )^2 R^2 dot %theta = left ( m_2 over { m_1 + m_2 } right )^2 h = h_1 newline R_2^2 dot %theta = left ( m_1 over { m_1 + m_2 } right )^2 R^2 dot %theta = left ( m_1 over { m_1 + m_2 } right )^2 h = h_2
L = m_1 h_1 + m_2 h_2 = { m_1 m_2} over {m_1 + m_2 } h
a_1 = m_2 over { m_1 + m_2 } a `````````````````` n_1 = n_2 = n
E = { m_1 m_2 } over { m_1 +m_2 } C = - { { m_1 m_2 } over { m_1 +m_2 }} {G (m_1 + m_2)} over {2a} = -{{G m_1 m_2 } over {2a} }

---
Poincare’ action-angle variables
alignl %LAMBDA = %mu sqrt{ G (M_s +m) a } ````` ````````` %lambda = M + %varpi newline alignl %TAU = %LAMBDA ( 1 -sqrt{1 - e^2} ) ```````````````````` %gamma = - %varpi newline alignl Z = ( 1 - %TAU) ( 1 - cos i ) ```````````%sigma = - %OMEGA
Jacobian coordinates